Christian Barnes

Maulds Meaburn Parish Council

01st January 2021

Dear Christian,

Following my site visit to Maulds Meaburn village green I can offer the following observations regarding the trees and general condition. I have listed the recommended works as priority 1 and priority 2 depending on the nature of the location and works required.

T10 -  oak, large dead limb over foot path, recommend removal of limb. P2

T15 – Ash, continue monitoring for ash die back

T16 – Sycamore, historic decay and bark die back in several location, monitor for the next year and re assess in 12 months.

T17 – Horse Chestnut, historic decay and fungal bodies present, monitor crown with spring growth to assess vitality. Broken branch river side suggest removal.  P2

T18 – Norway Maple, crown raise roadside 5 meters P2

T101 – Copper Beech, remove tree tie and stake.  P2

T19 – Horse chestnut, historic decay and fungal bodies present, monitor crown with spring growth to assess vitality.

T20 – Horse chestnut, historic decay and fungal bodies present, monitor crown with spring growth to assess vitality.

T21 – Beech, remove tree cage to prevent tree damage.  P2

T4 – Beech, historic decay pockets evident, monitor

T5 – Oak, prune to clear bt wires by 2 meters  P2

T7 + 8 – Silver birch, slight lean monitor.

T79 – Sycamore, Remove dead wood over path.  P1

T67 – Sycamore, Remove snapped limb over road and dead wood roadside.  P1

T65 – remove dead wood roadside and slapped limb to rear.  P1

T86 – Horse chestnut, remove lower growth roadside to 5 meters.  P2

T94 – Crab apple, prune internal water shoots.  P2

T27 – Horse chestnut, remove snapped limb roadside.  P1

T33 – Sycamore, this tree has been in decline for a number of years and has historical decay from Ganoderma as well as soil compaction and disturbance from renovation of the adjacent old chapel. The risk to the adjacent property and highway would necessitate its removal as the tree is now becoming increasingly more unstable. P1

T92 – Cherry, remove tree stake  P2

T99 – Oak, remove current tree guard and replace with wooden protection fence to stop grazing damage. P2

Overall, the decline of the Horse Chestnuts on the village green continues with all trees showing increasing dead wood and decay to major limbs. The carful program of management has enabled them to be preserved and continuing maintance and assessment will they remain a valuable part of the village in the near future.

T33 by the old chapel has been declining for a number of years and I would suggest this is now removed from a safety aspect to the property and adjacent highway.

All the recommended work has been listed either priority 1 or 2 depending on the urgency of the works.

If you need any further information please don’t hesitate to contact me.

Yours sincerely

Steven Hodgson